## Slide 1: Printed Circuit Board Layout
Micro-SD Adapter (GR), Arduino (OR), Wi-fi Module (BL)
2-layer PCB connecting power and necessary signals for microcontroller to local memory, wi-fi module, digital, and analog inputs

## Slide 2: Local Sensor Module Mounts
Top cover has 4 mountable points for 4 separate sensors
Mounting mechanism is a guided sliding contact, reduces Degrees of Freedom from 6 to 1

## Slide 3: Remote Sensor Module Mounts
White block uses temporary adhesive (hot glue) to bind to vehicle surface
Sensor mount can fasten using M3 screw to tapped hole on the white block

## Slide 4: Electrical Quick Disconnect
JST style connector between sensor mounts and terminal blocks
Supports reliable and efficient connection point between device and sensor

## Slide 5: Device Mount
Device has 2 clip style connectors for DIN rail
2 holes on a flat plane to mount device to DIN rail using M5 screws and tapped holes
Functionally flexible; designed for on-vehicle test and benchtop test processes

## Slide 6: Graphical User Interface
Guides members of all experience levels through a common test procedure

## Slide 7: Result Dashboard
Members can access a highly visual dashboard to view test results and test performance indicators
Connected to Microsoft Azure database

## Slide 8: Verification and Validation Plans
Formula Electric team will test in the immediate future (Before end of February
  Cooling system tests: measuring pressure, temperature, and flow rate
  Dynamometer tests: measuring rotational speed and torque
Capstone team will test in the immediate future (coming week). Ensure functional requirements were met robustly
  Dynamic process tests (driving using a personal car): acceleration in X/Y/Z, temperature, and humidity
  Replacing in-scope sensors with other Arduino compatible sensors to test device sensor flexibility
  Edge case test device: Extremely short test, long tests, atypical interactions with GUI, atypical sign-in attempts, etc.